## Slide 1: Locating and Tracking BLE Beacons with Smartphone
Dongyao Chen, Kang G. Shin, Yurong Jiang, and Kyu-Han Kim
Seoul/Incheon, South Korea
December 14, 2017

## Slide 2: Background: BLE Beacon
BLE beacon: a class of BLE devices that broadcast their IDs to nearby devices
  Light-weighted, low-power design (2-year battery life)
Main usage scenario: measuring proximity in a retailor store
Estimated market of $52B by year 2020
Chart: US Beacon Installed Base Forecast[1]
| 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0 | 2018.0
Installation (thousands) | 4.3 | 100 | 150 | 600 | 1500 | 4200
[1] http://www.businessinsider.com/google-looks-to-secure-bluetooth-beacon-communications-2016-4

## Slide 3: Background: Proximity Sensing App
User’s smartphone can estimate the proximity of neighboring BLE beacons by analyzing RSS
Band pass filter
AGC
Mixer
AMP
RSS reading
Analog front end
DSP back end
BLE signal
Preamble (9 B)
UUID (16 B)
Major (2 B)
Minor (2 B)
TX (1 B)
Broadcast periodically
30 Bytes

## Slide 4: Background: Proximity Sensing App
Immediate
Far
Near
User’s smartphone can estimate the proximity of neighboring BLE beacons by analyzing RSS
Provide rough proximity information of surrounding beacons
  E.g., immediate, near, and far

## Slide 5: Background: Proximity Sensing App
YOUR ITEM IS “NEAR” !
I
Legacy Proximity Application…
User’s smartphone can estimate the proximity of neighboring BLE beacons by analyzing RSS
Provide rough proximity information of surrounding beacons
  E.g., immediate, near, and far
Usability is limited – only proximity information is provided
YOUR ITEM’s POSITION IS () !!
II
LocBLE

## Slide 6: Benefits from Estimating Beacons’ Location
Use-cases
  Locate lost item(s)
  Highlight interested item(s) in AR
  Infer user’s relative location
  “Last meter” navigation: fine-grained localization for augmenting GPS navigation
“Last meter” navigation
Infer user’s relative location
Interested item
Highlight item in AR
Find item

## Slide 7: Locating BLE Beacons – why it’s Challenging?
Constraints stem from the nature of BLE beacon signal
  Limited transmission power – for sustaining years of usage
  Narrow bandwidth – only 2 MHz bandwidth for each sub-channel
  Limited connectivity – only capable of sensing BLE advertisements
v. s.
< 500 mA·h battery designed for 3-year lifetime
AC powered RF transmitter
Bandwidth: 40 MHz for 802.11 n
Bandwidth for BLE signal 2 MHz ea. sub-channel
Connectivity: only send
Connectivity: both send and receive

## Slide 8: Goal: Locating BLE Beacon on Smartphones
Smartphone-based application for estimating location of nearby commodity BLE beacons
LocBLE

## Slide 9: Goal: Locating BLE Beacon on Smartphones
Smartphone-based application for estimating location of nearby commodity BLE beacons
3 key modules
LocBLE
RSS data preprocessing
RSS + IMU
sensor fusion
Beacon clustering

## Slide 10: I: Mitigate RSS Signal Fluctuation
RSS – distance (path loss) model:
Estimate path loss exponent and path loss offsets
  Path loss exponent – varies with environment
  Path loss offsets – vary with environment and hardware configuration(s)
Notes: Here we use the Log distance path loss model
First takeaway is RSS data is noisy. The noise comes two factors from the rayleigh fading model
U
  Different models of Bluetooth device will cause drift of distance estimation
PL(d0)PL(d0) = Path Loss in dBdB at a distance d0d0 PLd>d0PLd>d0= Path Loss in dBdB at an arbitrary distance dd nn = Path Loss exponent. See the table below that gives the path loss exponent for various environments. χχ = A zero-mean Gaussian distributed random variable (in dBdB) with standard deviation – σσ. This variable is used only when there is a shadowing effect. If there is no shadowing effect, then this variable is zero. Taking log of the Normal (Gaussian)-variable results in the name “Log-Normal” fading.
Unknown 𝑣𝑎𝑟𝑖𝑎𝑏𝑙𝑒𝑠: 𝐸_1+𝐸_2
  Different models of Bluetooth device will cause drift of distance estimation

## Slide 11: II. RSS + IMU Sensor Fusion
BLE beacon
Observer
Problem formulation: RSS reading + user’s movement
Estimate target
Measured by BLE receiver

## Slide 12: II. RSS + IMU Sensor Fusion
BLE beacon
Observer
Problem formulation: RSS reading + user’s movement
Measured by BLE receiver
Measured by IMU sensor
Estimate target

## Slide 13: II. RSS + IMU Sensor Fusion
BLE beacon
Observer
Problem formulation: RSS reading + user’s movement
Measured by observer’s/target’s IMU sensor
Notes: Motivated by triangulation.
Specifically, users

## Slide 14: II. RSS + IMU Sensor Fusion
“L-shaped” movement process
  Resolve symmetric issue
  Accumulate enough data for sensor fusion
A
B
C
BLE Beacon
Ambiguity 1
BLE Beacon
Actual location
BLE Beacon
Ambiguity 2

## Slide 15: III. Clustering Algorithm
Refine estimation results by leveraging neighboring beacons
Clustering
  Formulate cluster based on dynamic time warping (DTW) distance
Far-fetch beacons
Neighboring beacons
Notes: Our goal here is not for separating beacons.
People may misunderstand that, say two bus stop signs are close to each other

## Slide 16: Evaluation
Implementation:
  LocBLE on both Android and iOS platforms
  Tested on iBeacon protocol
  9 experimental environments
Notes: remove 7, 8, 9

## Slide 17: Evaluation
Estimating stationary beacons’ locations
Chart: Estimation error (m)
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0
x est. | 0.75 | 1.4 | 1.55 | 1.69 | 1.71 | 1.88
h est. | 0.65 | 1.3 | 1.45 | 1.55 | 1.65 | 1.8
LocBLE abs. | 0.98 | 1.9 | 2.1 | 2.3 | 2.35 | 2.55
Dartle app | 1.56 | 3.1 | 3.56 | 3.5 | 4.12 | 5.21
Notes: xlabel
explain x and h are coordinates

## Slide 18: Evaluation
Changing RSS sampling frequency
Varying length of data trace for location estimation
Notes: Explain CDF
Explain length of data trace, extimation error is x & h

## Slide 19: Evaluation
Clustering Performance: estimations from neighboring devices mitigate the impact of noisy RSS readings
Chart: Number of beacons
| 1.0 | 2.0 | 4.0 | 6.0
Lab | 3.11 | 2.592 | 1.811 | 1.453
Hall | 2.661 | 2.322 | 1.556 | 1.198

## Slide 20: Conclusion
Smartphone-based application for estimating location of nearby commodity BLE beacons
3 key components for extracting location information
  RSS signal preprocessing
  RSS + IMU sensor fusion
  Clustering
Achieved ~2 m localization accuracy in various environment
LocBLE

## Slide 21: Thank you
Q & A
Find it with locble!
Ugh, I lost MY ble headset! have to use wired earbuds again!
Comic credit: Rich Stevens @ imore.com

## Slide 22: References
Dongyao Chen, Kyong-Tak Cho, Sihui Han, Zhizhuo Jin, and Kang G. Shin. Invisible Sensing of Vehicle Steering with Smartphones. In ACM MobiSys, 2015.
Nirupam Roy, He Wang, and Romit Roy Choudhury. I am a Smartphone and I can Tell my User’s Walking Direction. In ACM MobiSys, 2014.
Souvik Sen,Jeongkeun Lee,Kyu-Han Kim,and Paul Congdon. Avoiding Multipath to Revive Inbuilding WiFi Localization. In ACM MobiSys, 2013.
Yuanchao Shu, Kang G Shin, Tian He, and Jiming Chen. Last-mile Navigation Using Smartphones. In ACM MobiCom, 2015.
P. Bahl and V. N. Padmanabhan. Radar: an In-building RF-based User Location and Tracking System. In IEEE INFOCOM, 2000
Bluetooth 5.0 Core Specication, transmitter characteristics, page 2536. https://www.bluetooth.com/speci cations/adopted-specications.

## Slide 23: Backup slides

## Slide 24: Measurement Pipeline of LocBLE
Estimation result
Noise filtering
Data fusion
Environment analysis
Motion tracker
Motion Sensor
BLE Scanner
Magnetometer
Regression-based sensor fusion
Preprocess RSS

## Slide 25: Discussion
LocBLE enables BLE beacon localization at low cost
LocBLE

## Slide 26
Backup slides

## Slide 27: Using RSS Signal for Sensing Location
RSS – distance model
Fading coefficient n
  Estimate n, instead using a preset value
  E.g., n = 2 for outdoor case
U
  Different models of Bluetooth device will cause drift of distance estimation
RSS

## Slide 28
YOUR ITEM IS “NEAR” !
I
YOUR ITEM’s POSITION IS () !!
II
With LocBLE
Legacy Proximity Application…

## Slide 29
Data collection layer
Location estimation layer
Calibration layer
Nodes clustering
Adaptive calibration
Is target moving?
Noise filtering
Data fusion
EnvAware
Motion tracker
Motion Sensor
BLE Scanner
Magnetometer